## Slide 1: EE3014/IM3001 DSP Lab Digital Signal Processing and Applications

## Slide 2: Objective
To learn different signal representations of audio signals, and to design filters to remove the noise.

## Slide 3: A. Frequency Spectrum of Audio Signals
Copy the noisy audio file based on your seat number from D:\EE3014 to the desktop or an working folder.
Read the data from the noisy audio file using MATLAB function audioread().
Audio file read:
[audio, samplingfrequency] = audioread(‘filename’);

## Slide 4
Plot the Fourier magnitude spectrum of this noisy audio data in MATLAB. The k-th fft coefficient should map to k*fs/N actual frequency, where N is the length of the FFT and fs is the sampling frequency.
DFT (FFT) of audio: spectrum = fft(audio);
Plot of the magnitude spectrum:
plot(frequencyaxis, magnitudespectrum);
Let be the length of the audio vector. For -point DFT, the DFT index denotes a frequency . Therefore, the frequency axis is:
frequencyaxis = samplingfrequency*[0:N-1]/N;
Absolute value since spectrum is complex:
magnitudespectrum = abs(spectrum);

## Slide 5
Sketch the magnitude spectrum of the noisy audio on the answer sheet, and indicate where the noise is in the spectrum.
Sample frequency spectrum

## Slide 6: B. Filter Design to Remove Noise
Design filter(s) to remove the noise identified in section A from the noisy audio. Try out different filter parameters to obtain good filtered output. For filter design, use the normalized frequency which is equal to the actual frequency (f) divided by fs/2 (Nyquist frequency), where fs is the sampling frequency.
Write down the type (e.g. low-pass, high-pass, etc.) and the frequency parameters (e.g. cut-off frequencies) of the designed filter(s).

## Slide 7
FIR filter design:
numerator = fir1(order, cutoff, ‘filtertype’);
order = 50
cutoff = single frequency, or vector of two cutoff frequencies
‘filtertype’ = ‘low’ or ‘high’ or ‘bandpass’ or ‘stop’
numerator = filter coefficients (impulse response)
Filter Design
IIR notch filter design:
[numerator, denominator] = iirnotch(notchfrequency, bandwidth);
notchfrequency = normalized frequency
bandwidth = 0.01
numerator = coefficients of numerator polynomial of H(z)
denominator = coefficients of denominator polynomial of H(z)

## Slide 8
Lowpass example
Bandstop example
Notch example
Examples

## Slide 9
Filter visualization:
magnitude & phase response, group delay, impulse response, step response, pole-zero plot, filter coefficients
fvtool(numerator) for FIR
fvtool(numerator, denominator) for IIR
Filter Visualization

## Slide 10
Obtain the filtered audio and sketch the magnitude spectrum of this audio.
Filtering:
audiooutput = filter(numerator, denominator, audioinput);
denominator = 1 for FIR

## Slide 11
Listen to the original noisy and the filtered audios using sound(). Describe the audio quality difference between the two audios.
Audio playback:
sound(audio, samplingfrequency)
soundsc(audio, samplingfrequency)

## Slide 12: Submission
Hand in the answer sheet at the end of the lab session.